## Slide 1
SLIDE 01 // PROJECT VISION & PITCH
WAYZE
Offline-First Indoor Navigation & Hazard Alert for Visually Impaired Users
Core Mission
A supplement to the white cane, never a replacement. Real-time edge AI navigation that works completely offline with the screen OFF.
Key Innovation
Quantized YOLOv8n running directly on budget phone CPU (XNNPACK). Zero cloud bill. Zero image storage. Sub-70ms target latency.
Founding Team
Student Builders & Embedded Engineers | India Contact: founder@wayze.in | Open-source Core
🗣️ SPEAKER HINGLISH CUE: "Namaste judges. Humne banaya hai Wayze: 100% offline indoor navigation jo white cane ka sahayak hai, uska badal nahi."
Notes: SPEAKER SCRIPT:
Namaste judges. Humne banaya hai Wayze: 100% offline indoor navigation jo white cane ka sahayak hai, uska badal nahi.
SLIDE OBJECTIVE:
Offline-First Indoor Navigation & Hazard Alert for Visually Impaired Users

## Slide 2
SLIDE 02 // THE PROBLEM
The Indoor Blind Mobility Gap
Why the white cane and cloud AI both leave users vulnerable
White Cane Limit: 1 Meter Ground Only
• Cannot detect chest/head-height hazards: open cupboards, signs, hanging wires. • Zero directional guidance: cannot tell 'door is 3m straight, then turn left'.
Cloud Vision AI is Too Slow & Expensive
• 250ms - 800ms network lag causes staircase falls. • 0.9 GB data/hour exhausts budget mobile plans in 90 minutes. • $2-5/month server fees make it unaffordable for Indian users.
No Indoor GPS Exists
• Satellite GPS signals do not penetrate concrete roofs. • Indoor beacons/tags are absent in 99% of Indian homes and public spaces.
🗣️ SPEAKER HINGLISH CUE: "White cane zameen ke liye best hai par head-level hazards nahi dekhta. Aur cloud AI 500ms lag karta hai jo indoor safety mein dangerous hai."
Notes: SPEAKER SCRIPT:
White cane zameen ke liye best hai par head-level hazards nahi dekhta. Aur cloud AI 500ms lag karta hai jo indoor safety mein dangerous hai.
SLIDE OBJECTIVE:
Why the white cane and cloud AI both leave users vulnerable

## Slide 3
SLIDE 03 // WHO IT'S FOR
The Reality of Budget Indian Smartphones
Designing for the bottom 95% of visually impaired users
Target Device Profile
• Sub-₹12,000 Android phones ($140). • 3GB to 4GB RAM total. • MediaTek Helio G85 / Snapdragon 680. • Cortex-A55 efficiency CPU cores.
Interaction Reality
• Users cannot stare at screens or tap tiny buttons. • Phone is worn on a chest lanyard. • Screen must stay completely OFF. • Audio via earbud + heavy tactile haptics.
Hardware Constraint
• User has NO smart cane today. • App MUST function in 'Phone-Only Mode' now. • Future BLE cane must connect with zero app logic changes.
🗣️ SPEAKER HINGLISH CUE: "India ke majority blind users budget 4GB RAM phones use karte hain. Unke liye humne screen-off, phone-only offline navigation banayi hai."
Notes: SPEAKER SCRIPT:
India ke majority blind users budget 4GB RAM phones use karte hain. Unke liye humne screen-off, phone-only offline navigation banayi hai.
SLIDE OBJECTIVE:
Designing for the bottom 95% of visually impaired users

## Slide 4
SLIDE 04 // THE SOLUTION
Wayze: Offline Edge AI Co-Pilot
An intelligent situational awareness layer that respects the white cane
100% On-Device Edge AI
YOLOv8n quantized to INT8 running locally on ARM CPU via XNNPACK. Target 40-70ms inference. $0 cloud bill. Airplane-mode operational.
Room Graph Dijkstra
Pre-mapped topological room graph in private SQLite storage. Calculates step-by-step spoken instructions: '5 steps straight, turn left'.
Sensor Fusion & Drop-Off Protection
Fuses vision threat scores with downward range sensors. Detects staircase drop-offs in <100ms with P0 preemption.
🗣️ SPEAKER HINGLISH CUE: "Wayze local CPU pe chalta hai, room graph se rasta batata hai, aur seedhi ya obstacle aane par turant heavy vibration alert deta hai."
Notes: SPEAKER SCRIPT:
Wayze local CPU pe chalta hai, room graph se rasta batata hai, aur seedhi ya obstacle aane par turant heavy vibration alert deta hai.
SLIDE OBJECTIVE:
An intelligent situational awareness layer that respects the white cane

## Slide 5
SLIDE 05 // SYSTEM ARCHITECTURE
Production Architecture: Kotlin + Flutter
Separation of real-time camera memory from high-level state logic
Native Android Layer (Kotlin)
• CameraX 30 FPS with STRATEGY_KEEP_ONLY_LATEST. • Direct ByteBuffer zero-alloc YUV to RGB letterbox 320x320. • TFLite with 2-thread XNNPACK delegate. • Foreground Service with PARTIAL_WAKE_LOCK.
Flutter Domain Layer (Dart)
• IoU + Kalman Tracker across frames. • Horizontal Field of View (HFOV) Zone Mapping. • Sensor Fusion Engine (Vision + Phone IMU + Cane). • In-Memory Dijkstra Navigation Graph in SQLite.
User Experience Layer
• Offline Vosk Hindi + English Speech Recognition. • Alert Priority Queue (P0 Danger, P1 Nav, P2 Info). • Multi-modal outputs: Android TTS + Haptic feedback patterns.
🗣️ SPEAKER HINGLISH CUE: "Camera aur ML native Kotlin mein RAM ke andar chalte hain, aur state machine, alerts, aur graph routing Flutter Dart mein handle hoti hai."
Notes: SPEAKER SCRIPT:
Camera aur ML native Kotlin mein RAM ke andar chalte hain, aur state machine, alerts, aur graph routing Flutter Dart mein handle hoti hai.
SLIDE OBJECTIVE:
Separation of real-time camera memory from high-level state logic

## Slide 6
SLIDE 06 // VISION PIPELINE
Image-to-Alert: 6-Stage Processing
From raw camera frame in RAM to spoken prompt in <100 milliseconds
1. Zero-Allocation Capture
CameraX captures YUV420 frame -> directly letterboxed into preallocated 320x320 buffer in RAM. Never saved to flash.
2. INT8 Inference & NMS
TFLite runs on CPU via XNNPACK (40-70ms target) -> produces [1, 4+nc, 2100] tensor -> class-wise NMS at IoU 0.45.
3. Zone & Threat Scoring
HFOV bearing angle: Left (<-12°), Center (±12°), Right (>+12°). Threat Score = Zone + Area Growth + Bottom-Y floor position.
4. Temporal Confirmation
2-3 consecutive confirming frames required before alert fires. Prevents false alarms from camera jitter.
🗣️ SPEAKER HINGLISH CUE: "Frame RAM mein preprocess hota hai, model infer karta hai, zone math lagta hai, aur 2-3 frame confirm hone ke baad hi alert bolta hai."
Notes: SPEAKER SCRIPT:
Frame RAM mein preprocess hota hai, model infer karta hai, zone math lagta hai, aur 2-3 frame confirm hone ke baad hi alert bolta hai.
SLIDE OBJECTIVE:
From raw camera frame in RAM to spoken prompt in <100 milliseconds

## Slide 7
SLIDE 07 // HARDWARE & FUSION
Sensor Fusion & The Smart Cane
Combining optical vision with direct distance measurements
The Glass Door Rule
Cameras see clear path, but cane ultrasonic detects solid barrier <50cm. Fusion Engine overrides vision -> Fires immediate P0 Alert: 'Obstacle 40cm ahead'.
Stairs Down Drop-Off Rule
Downward ground range normal = 110cm. If downward distance > 145cm for >= 2 consecutive samples: Triggers P0 Emergency: 'Stairs down ahead. Stop.'
Smart Cane Hardware (Simulated)
• ESP32-S3 microcontroller with BLE 5.0. • VL53L1X ToF (downward) + Ultrasonic (front). • Haptic grip motor + 18650 Li-ion battery. • Target BOM: $19.20 @ 10,000 units (~₹1,600).
🗣️ SPEAKER HINGLISH CUE: "Kaanch ke darwaze pe camera dhokha kha sakta hai, par cane ka sensor pakad leta hai. Downward sensor 145cm se zyada hote hi seedhi ka alert deta hai."
Notes: SPEAKER SCRIPT:
Kaanch ke darwaze pe camera dhokha kha sakta hai, par cane ka sensor pakad leta hai. Downward sensor 145cm se zyada hote hi seedhi ka alert deta hai.
SLIDE OBJECTIVE:
Combining optical vision with direct distance measurements

## Slide 8
SLIDE 08 // AUDIO & VOICE INTELLIGENCE
Voice Engine & Alert Prioritization
Delivering critical cues without fatiguing the blind user
P0 Danger (Emergency)
Drop-off, stairs down, obstacle <50cm. Flushes lower queue, INTERRUPTS active TTS speech mid-word, fires 400ms heavy vibration.
P1 Navigation (Turn Guidance)
'Turn left in 3 meters'. Expires after 2 seconds if delayed. Double short vibration pulse (80ms + 80ms).
P2 Info & Cooldown
'Table on your right'. Spoken ONLY when system is fully idle. 3-second cooldown per (class, zone) prevents repetitive spam.
Offline Vosk Voice Assistant
Offline Hindi + English restricted grammar. 4-step repair ladder: Soft retry -> Guided options -> Yes/No confirm -> Hardware button fallback.
🗣️ SPEAKER HINGLISH CUE: "P0 alert aate hi active speech beech mein rukti hai aur heavy vibration bajta hai. 3 second cooldown faltu chatter rokta hai."
Notes: SPEAKER SCRIPT:
P0 alert aate hi active speech beech mein rukti hai aur heavy vibration bajta hai. 3 second cooldown faltu chatter rokta hai.
SLIDE OBJECTIVE:
Delivering critical cues without fatiguing the blind user

## Slide 9
SLIDE 09 // DATA PRIVACY & STORAGE
Privacy By Design: Zero Cloud, Zero Photos
Blind users have absolute right to private home surroundings
Camera Frames: RAM Only
Video frames exist only in volatile RAM buffers for ~33ms. Frames are immediately overwritten and discarded. Zero images saved to disk. Zero images sent to any server.
Local Sandboxed Storage
• Room Maps: Private SQLite database in app sandbox. • Settings: SharedPreferences (voice rate, language). • Logs: 5MB text-only rotating circular buffer (7 days max).
Optional Telemetry: Off by Default
No automatic cloud sync. User must explicitly opt-in to 'Improve the App'. Telemetry sends only text crash stack traces—never audio or video.
🗣️ SPEAKER HINGLISH CUE: "Koi bhi photo ya video phone memory mein save nahi hoti aur na internet pe jati hai. Sab kuch private local database mein rehta hai."
Notes: SPEAKER SCRIPT:
Koi bhi photo ya video phone memory mein save nahi hoti aur na internet pe jati hai. Sab kuch private local database mein rehta hai.
SLIDE OBJECTIVE:
Blind users have absolute right to private home surroundings

## Slide 10
SLIDE 10 // ENGINEERING TRADE-OFFS
Edge Compute: Why CPU Beats Mobile GPU
Avoiding thermal collapse and driver fragmentation on budget devices
The Mobile GPU/NNAPI Trap
Budget Helio G85 & Snapdragon 680 chips have fragmented, buggy NNAPI drivers. Mobile GPUs cause severe thermal throttling within 10 minutes.
ARM CPU + XNNPACK Solution
Pinned to 2 Cortex-A55 efficiency cores with hand-tuned ARM assembly. Deterministic execution, zero driver crashes, highly stable 40-70ms latency.
Stationary Adaptive Throttling
Phone IMU senses when the user stops walking. Inference drops automatically from 10 FPS to 4 FPS, cutting battery & heat by 60%.
🗣️ SPEAKER HINGLISH CUE: "Budget phones pe GPU aur NNAPI overheat hoke crash kar dete hain. Humne CPU XNNPACK chuna jo 100% stable rehta hai aur battery bachata hai."
Notes: SPEAKER SCRIPT:
Budget phones pe GPU aur NNAPI overheat hoke crash kar dete hain. Humne CPU XNNPACK chuna jo 100% stable rehta hai aur battery bachata hai.
SLIDE OBJECTIVE:
Avoiding thermal collapse and driver fragmentation on budget devices

## Slide 11
SLIDE 11 // FAIL-SAFE ENGINEERING
Life-Safety Reliability & Safe Mode
Core Rule: 'Silence never means safe'
2000ms Vision Watchdog
If camera freezes for >2s, automatically restarts vision pipeline up to 3x. If restarts fail: 'Vision stopped. Sensor and map mode active.'
25-Second Heartbeat Tick
Periodic subtle haptic tick every 25 seconds while navigating. If the ticks stop, user immediately knows the app or phone has died.
Crash-Loop SAFE MODE
3 crashes in 5 minutes triggers permanent Safe Mode lockdown. Camera/voice killed. Giant tactile button. 'Wayze is in safe mode. Use your cane.'
🗣️ SPEAKER HINGLISH CUE: "Agar app shaant ho jaye toh user ko lag sakta hai rasta clear hai. Isiliye heartbeat tick aur 3-crash Safe Mode user ko protect karte hain."
Notes: SPEAKER SCRIPT:
Agar app shaant ho jaye toh user ko lag sakta hai rasta clear hai. Isiliye heartbeat tick aur 3-crash Safe Mode user ko protect karte hain.
SLIDE OBJECTIVE:
Core Rule: 'Silence never means safe'

## Slide 12
SLIDE 12 // COMPETITIVE LANDSCAPE
Market Comparison: Assistive Navigation
Why existing tools leave a massive accessibility gap
WeWALK Smart Cane
Price: ₹55,000+ ($600) [Verify before presenting]. High-end ultrasonic handle, but NO on-device computer vision, no room graph, requires cloud.
IIT Delhi SmartCane / UltraCane
Price: ₹3,500 - ₹10,000 [Verify before presenting]. Simple ultrasonic beeper on cane. No object recognition, no spoken turn directions.
Seeing AI / Be My Eyes
Price: Free (Software). Cloud scene description apps. Requires 4G/5G, 2-3s delay, photo taking. Not for real-time walking guidance.
WAYZE (Our Edge)
Price: App FREE / Future Cane Target BOM: ₹1,800 ($22). 100% Offline-first, on-device YOLOv8, Dijkstra room graph, drop-off fusion, screen-off operation.
🗣️ SPEAKER HINGLISH CUE: "WeWALK ₹55,000 ki hai aur Seeing AI cloud pe chalta hai. Wayze offline phone app free deta hai aur future cane sirf ₹1,800 target karti hai."
Notes: SPEAKER SCRIPT:
WeWALK ₹55,000 ki hai aur Seeing AI cloud pe chalta hai. Wayze offline phone app free deta hai aur future cane sirf ₹1,800 target karti hai.
SLIDE OBJECTIVE:
Why existing tools leave a massive accessibility gap

## Slide 13
SLIDE 13 // VERIFICATION MATRIX
The Honesty Board: Verified vs Targets
Engineering transparency: Separating proven code from hardware goals
VERIFIED & WORKING NOW
• 109 automated unit & integration tests passing. • Alert priority preemption, 3s cooldown, drop-off rule logic. • Offline Vosk Hindi/English intent matcher & repair ladder. • SQLite atomic map writes with .bak restoration.
TARGETS & ESTIMATES (To Be Measured on Hardware)
• Inference latency target: 40-70 ms on Snapdragon 680. • Battery drain estimate: ~8-14% per hour continuous analysis. • Smart cane BOM estimate: $19.20 @ 10,000 units. • Lab validation accuracy: 75.5% mAP@50 (model_facts.json).
WHAT IS NOT DONE YET
• NO physical smart cane fabricated yet (architecture simulated). • NO clinical blind-user field trials conducted yet. • Phase 2 milestone: 50 visually impaired student pilot.
🗣️ SPEAKER HINGLISH CUE: "109 tests passing hain, software pipeline ready hai. Par humne abhi tak cane fabricate nahi ki hai aur blind user testing Phase 2 mein honi hai."
Notes: SPEAKER SCRIPT:
109 tests passing hain, software pipeline ready hai. Par humne abhi tak cane fabricate nahi ki hai aur blind user testing Phase 2 mein honi hai.
SLIDE OBJECTIVE:
Engineering transparency: Separating proven code from hardware goals

## Slide 14
SLIDE 14 // LIVE DEMONSTRATION
Live Demonstration Architecture
5-minute offline verification using real Android phone
1. Airplane Mode Verification
Wi-Fi & Data OFF. Hardware Volume-Up pressed -> speaks 'Where am I' instantly using offline Vosk engine.
2. Real-Time Vision & Zones
Camera points at chair -> Live bounding box overlay -> p50 latency counter -> Left/Center/Right zone pan.
3. P0 Danger Preemption Test
Navigation speaks -> Mock cane distance pulled to 35cm -> Immediate voice cut, heavy 400ms buzz, 'Obstacle ahead stop!'.
🗣️ SPEAKER HINGLISH CUE: "Demo mein hum airplane mode show karenge, live chair bounding box dekhenge, aur 40cm pe speech cut hoke heavy vibration prove karenge."
Notes: SPEAKER SCRIPT:
Demo mein hum airplane mode show karenge, live chair bounding box dekhenge, aur 40cm pe speech cut hoke heavy vibration prove karenge.
SLIDE OBJECTIVE:
5-minute offline verification using real Android phone

## Slide 15
SLIDE 15 // COMMERCIAL SCALABILITY
Unit Economics & 4-Phase Roadmap
From open-source software to institutional subsidized hardware
Unit Economics @ Scale
• Cloud Inference Bill: $0.00 / month. • Static Map CDN / Crashlytics: $0.05 - $0.40 / user / month. • Smart Cane BOM: $19.20 (~₹1,600) @ 10k units.
Phase 1 & 2 (Now - Month 4)
• Phase 1: Complete offline Android app & test harness (DONE). • Phase 2: 50-user Blind School pilot (NAB Delhi / BPA Ahmedabad).
Phase 3 & 4 (Month 5 - 12)
• Phase 3: 100 prototype canes fabrication, WPC/BIS safety certification. • Phase 4: B2G ADIP Scheme subsidy & transit hub indoor map packs.
🗣️ SPEAKER HINGLISH CUE: "Inference bill zero hai. Phase 2 mein 50 blind students ke saath pilot karenge, aur Phase 3 mein 100 cane prototypes fabricate karenge."
Notes: SPEAKER SCRIPT:
Inference bill zero hai. Phase 2 mein 50 blind students ke saath pilot karenge, aur Phase 3 mein 100 cane prototypes fabricate karenge.
SLIDE OBJECTIVE:
From open-source software to institutional subsidized hardware

## Slide 16
SLIDE 16 // THE ASK
The Ask: Empowering Independence
Assisting blind mobility with dignity, speed, and safety
Grant Funding: ₹15 Lakhs ($18,000)
• ₹6 Lakhs (40%): 100 Smart Cane prototype fabrication & tooling. • ₹5 Lakhs (33%): 50-user Blind School trials & localized voice datasets. • ₹4 Lakhs (27%): WPC / BIS wireless certification & ground truth testing.
Mentorship & Institutional Access
Seeking connections with National Association for the Blind (NAB), rehabilitation clinics, and assistive hardware manufacturing mentors.
Our Closing Commitment
White canes taught them to walk. Wayze will teach them to walk without fear. Thank you! We are ready for your questions.
🗣️ SPEAKER HINGLISH CUE: "Hume ₹15 Lakhs ka grant aur Blind Schools ke saath pilot connects chahiye. Safed chhadi ne unhe chalna sikhaya, Wayze unhe aazadi dega."
Notes: SPEAKER SCRIPT:
Hume ₹15 Lakhs ka grant aur Blind Schools ke saath pilot connects chahiye. Safed chhadi ne unhe chalna sikhaya, Wayze unhe aazadi dega.
SLIDE OBJECTIVE:
Assisting blind mobility with dignity, speed, and safety